## Slide 1: Modelling and Exploration of Coarse-Grained Reconfigurable Arrays: Using the Open-Source CGRA-ME Framework
Omar Ragheb, Stephen Wicklund, Kentaro Sano1, Jason Anderson DATE’24 Tutorial, Valencia, Spain
March 26, 2024

## Slide 2: CGRA Challenges
Architectures less studied than competing platforms, such as FPGAs or GPGPUs
CAD tool development required
FPGAs:
Verilog-to-Routing
GPUs:
GPGPU-Sim
CGRAs: ???
Processors: gem5
Notes: - why cgra

## Slide 3: Introduction to CGRA-ME
CGRA-ME: an open-source modelling and exploration framework for CGRA architecture and CAD exploration
Objectives:
  Allow an architect to model a wide range of CGRA architectures via a C++ API
  Allow an application, described in a high-level language, to be mapped onto the modelled CGRA
  Area, performance, and power modelling of the CGRA for an application
This allows for:
  Simulation and verification of application on modelled CGRA
  Physical realization of CGRA as an ASIC or FPGA overlay

## Slide 4
CGRA-ME: Framework
CGRA Architecture Description
CGRA Architecture Interpreter
Device Model of Architecture
Verilog Simulation
Std. Cell Synthesis Place and Route
FPGA Synthesis Place and Route
Standard-Cell CGRA Perf, Power & Area
FPGA-Overlay CGRA Perf, Power & Area
LLVM
Mapper
Data-Flow Graph of Application
Benchmark
Verilog RTL for CGRA
Bitstream
Functional Verification
Architecture Constraints
Notes: Xander starts here

## Slide 5
CGRA-ME: Inputs
CGRA Architecture Description
Benchmark
CGRA-ME Framework takes in three input files which are:
Benchmark:
  C code application that needs acceleration
  Example benchmarks are machine learning, signal processing, image processing, …
Architecture Constraints:
  A constraint file that specifies the routing constraints and the fixed ports.
Architecture description:
  A C++ description of an CGRA architecture (specified using CGRA-ME’s API)
Architecture Constraints
Notes: Xander starts here

## Slide 6
CGRA-ME: Architecture Description
CGRA Architecture Description
CGRA Architecture Interpreter
Device Model of Architecture
Verilog Simulation
Std. Cell Synthesis Place and Route
FPGA Synthesis Place and Route
Standard-Cell CGRA Perf, Power & Area
FPGA-Overlay CGRA Perf, Power & Area
LLVM
Mapper
Data-Flow Graph of Application
Benchmark
Verilog RTL for CGRA
Bitstream
Functional Verification
Architecture Constraints
Notes: Xander starts here

## Slide 7: Architecture Description
As a user of CGRA-ME, there are two aspects of architecture that you need to describe
The first is the content of the Processing Element (PE)
The second is the PE matrix and the interconnect connecting the constituent PEs.

## Slide 8: RIKEN PE – Instantiate Submodules
IMM
fork
Join
FP Wrapper
Crossbar (SB)
buff A
buff B
buff Out
MUX A
MUX B
addSubModule(new ElasticBufferFIFO(“buff_A", loc, buffer_depth, 32));
addSubModule(new ElasticBufferFIFO(“buff_b", loc, buffer_depth, 32));
addSubModule(new Multiplexer(“MUX_A", loc, num_inputs + 2));
addSubModule(new Multiplexer(“MUX_B", loc, num_inputs + 2));
addSubModule(new ConstUnit(“IMM", loc, 32));
addSubModule(new ElasticFPFuncUnit(“FPALU", loc, Op-list, 32, latency));

## Slide 9: RIKEN PE – Interconnect Modelling
IMM
Join
FP Wrapper
buff A
buff B
buff Out
MUX A
MUX B
connectPorts(“crossbar.out” + num_outports - 1, “buff_A.in”, isElastic);
connectPorts(“crossbar.out” + num_outports, “buff_B.in”, isElastic);
connectPorts(“buff_A.out”, “MUX_A.in0”, isElastic);
connectPorts(“buff_B.out”, “MUX_B.in0”, isElastic);
connectPorts(“MUX_A.out”, “join.in0”, isElastic);
connectPorts(“MUX_B.out”, “join.in1”, isElastic);
Crossbar (SB)
fork

## Slide 10: RIKEN PE – Add Configuration Bits
IMM
Join
FP Wrapper
buff A
buff B
buff Out
MUX A
MUX B
addConfig(“MUXAConfig”, {“MUX_A.select”}, isElastic);
addConfig(“MUXBConfig”, {“MUX_B.select”}, isElastic);
addConfig(“IMMForkConfig”, {“Imm_fork.enable_downstream”}, isElastic);
addConfig(“IMMConfig”, {“Imm.in”}, isElastic);
addConfig(“FPALUConfig”, {“FPALU.select”}, isElastic);
Crossbar (SB)
fork

## Slide 11: Main C++ Function Calls
Instantiating submodules
addSubModule(new $(Module Class)($(Name), $(location), $(other args)));
Connecting ports
connectPorts($(Source Port Name), $(Sink Port Name), $(elastic bool));
Adding configuration bits
addConfig($(Config Name), $(Config Port Name), $(elastic bool));

## Slide 12: CGRA – Instantiate PE Matrix
for (unsigned int c = 0; c < cols; c++) {
for (unsigned int r = 0; r < rows; r++) {
addSubModule(new ProcessingElement(“PE_“ + r + c));
}
}

## Slide 13: CGRA – Instantiate PE Matrix
Next steps for a full architecture model:
  Interconnect the PE Matrix
  Add IO ports
  Add Memory Ports
IO Port
IO Port
IO Port
IO Port
Mem Port
Mem Port
Mem Port
Mem Port

## Slide 14: CGRAs Modelled within CGRA-ME
There are three main CGRAs modelled within CGRA-ME 2.0 release
  ADRES
  HyCUBE
  RIKEN
ADRES
Elastic RIKEN

## Slide 15: Architecture Modelling Summary
CGRA-ME provides a C++ API that allows one to:
  Instantiate a variety of primitives
    ALUs, Constants, Buffers, Registers, …
  Connect primitives to one another:
    Crossbars, Direct connections, MUXes, …
  Add configurability for the interconnect/primitives
With API, one can model wide range of different CGRAs
Limitations/ongoing work:
  Modelling predication, mixed bitwidth CGRAs and etc.

## Slide 16
CGRA-ME: DFG generation
CGRA Architecture Description
CGRA Architecture Interpreter
Device Model of Architecture
Verilog Simulation
Std. Cell Synthesis Place and Route
FPGA Synthesis Place and Route
Standard-Cell CGRA Perf, Power & Area
FPGA-Overlay CGRA Perf, Power & Area
LLVM
Mapper
Data-Flow Graph of Application
Benchmark
Verilog RTL for CGRA
Bitstream
Functional Verification
Architecture Constraints
Notes: Xander starts here

## Slide 17: DFG Extraction CGRA-ME
Front-end data-flow graph extraction -- LLVM
  State-of-the-art compiler used by Apple, NVIDIA, Xilinx, Intel, etc
  Leverage LLVM language support, parsing and optimizations
In LLVM, the program is represented in an Intermediate Representation (IR)
  Machine-independent assembly code
  Limited instruction set: add, xor, branch, mul, div
Target inner-loop kernels for mapping to CGRAs

## Slide 18: Data-Flow Graph Extraction
//DFGLoop: loop : marks the loop to be extracted

## Slide 19: Data-Flow Graph Visualization
DFG is a directed graph made up of:
  Nodes N
Const0
i6_add
i4_load
i5_add
i5_output

## Slide 20: Data-Flow Graph Visualization
DFG is a directed graph made up of:
  Nodes N
  Edges E
Const0
i6_add
i4_load
i5_add
i5_output

## Slide 21
CGRA-ME: Device Model Graph
CGRA Architecture Description
CGRA Architecture Interpreter
Device Model of Architecture
Verilog Simulation
Std. Cell Synthesis Place and Route
FPGA Synthesis Place and Route
Standard-Cell CGRA Perf, Power & Area
FPGA-Overlay CGRA Perf, Power & Area
LLVM
Mapper
Data-Flow Graph of Application
Benchmark
Verilog RTL for CGRA
Bitstream
Functional Verification
Architecture Constraints
Notes: Xander starts here

## Slide 22: Device Model Graph: Nodes
Each node is in one of three types.
Functional node
  Represent units that execute instructions such as add, mul, PHI
Routing node
  Nodes that create links between different functional or memory nodes
Memory node
  Nodes that can store data for 1 or more clock cycles

## Slide 23: Device Model Graph: Modulo Routing Resource Graph (MRRG)
FU
REG
Example Block
Generalizable – handles multiple types of primitives
Piecemeal construction
Registers are handled differently
From previous clock cycle
To next clock cycle
Notes: Piecemeal construction – done one at a time over time

## Slide 24: LLVM IR-based Functional Units
We align the functionality specification of CGRA blocks with the LLVM IR computational instructions
The capabilities of the architecture are expressed in the same instruction set as the compiler to the architecture
FU
REG
Example Block
mul | add | mul->add

## Slide 25
CGRA-ME: Mapping
CGRA Architecture Description
CGRA Architecture Interpreter
Device Model of Architecture
Verilog Simulation
Std. Cell Synthesis Place and Route
FPGA Synthesis Place and Route
Standard-Cell CGRA Perf, Power & Area
FPGA-Overlay CGRA Perf, Power & Area
LLVM
Mapper
Data-Flow Graph of Application
Benchmark
Verilog RTL for CGRA
Bitstream
Functional Verification
Architecture Constraints
Notes: Xander starts here

## Slide 26: What is Mapping?
Mapping is finding the subset of the MRRG that the DFG can be embedded into.
The complexity of the mapping problem stems from aspects of both the application and the architecture:
  Long pipelines
  Limited interconnect in the architecture
Mapping is an interesting area of research, and within CGRA-ME 2.0, there are three main mappers:
  ILPMapper DAC’18
  Heuristic Mapper FCCM’19
  Clustered Mapper DAC’24

## Slide 27
CGRA-ME: Verification and Profiling
CGRA Architecture Description
CGRA Architecture Interpreter
Device Model of Architecture
Verilog Simulation
Std. Cell Synthesis Place and Route
FPGA Synthesis Place and Route
Standard-Cell CGRA Perf, Power & Area
FPGA-Overlay CGRA Perf, Power & Area
LLVM
Mapper
Data-Flow Graph of Application
Benchmark
Verilog RTL for CGRA
Bitstream
Functional Verification
Architecture Constraints
Notes: Xander starts here

## Slide 28
Verilog Generation (1)
Generate RTL for:
  Simulation / Verification
  Standard cell (ASIC) synthesis, placement and routing
  FPGA-overlay synthesis, placement and routing

## Slide 29: Verilog Generation (2)
Func. U.
C
io
io
Func. U.
C
ALU
ALU
Func. U.
C
C
ALU
ALU
CGRA
Take the module tree that the MRRG was generated from, and emit a parameterized Verilog file for each module type:
  Includes ports, sub-module declarations, and a generic implementation of the block.
Modules for configuration are also added to the parent module of their configuration target
  Automatically connected to the right module, and linked together to form an inter-module scan chain.
FU
IO
IO
IO
FU
FU
FU
FU
FU
FU
FU
FU

## Slide 30: Configuration Bitstream Generation
FU
REG
+
DFG
MRRG
Modules
A successful mapping associates all nodes and edges in the DFG with one or more MRRG nodes.
Iterate the mapped sub-modules, generate a configuration bitstream for the submodule of the application.

## Slide 31: Functional Verification
Configuration bitstream is emitted as part of a “configurator” Verilog module
Testbench instantiates configurator & CGRA, provides clock signal, etc.
Permits functional verification of the CGRA as configured for an application
Testbench
configurator.v
CGRA.v
CGRA-ME
ModelSim
Configuration Gen.
Verilog Gen.
benchmark.c

## Slide 32: Standard Cell CGRAs
Input CGRA Verilog RTL into ASIC flow
  Open source 45nm standard cell library
  Implementation is not optimal, but allows relative comparisons between architectures
Synthesized with Synopsys Design Compiler
Place and route with Cadence Innovus (floorplanned)
STA performed using Synopsys Prime Time
Floorplanned 4x4 ADRES CGRA in standard cells

## Slide 33: Thank You for Joining Us! https://cgra-me.ece.utoronto.ca/